## Slide 1: Compiler Laboratory
Prof. P. P. Das and Prof. I. Sengupta
September 3, 2020

## Slide 2: x86 Instruction Set Architecture Compiling C code to x86 Assembly

## Slide 3: Introduction to x86 Architecture
Totally dominates laptop/desktop/server market.
Evolutionary design:
  Backward compatible till 8086 (introduced in 1978).
Based on Complex Instruction Set Computer (CISC) architecture.
  Many different instructions with a number of variations.
  The alternate is the Reduced Instruction Set Computer (RISC) architecture.

## Slide 4: Evolution of x86 Architecture
Name | Date | Clock | Features
8086 | 1978 | 5-10 MHz | First 16-bit Intel processor 1MB address space
80386 | 1985 | 16-33 MHz | First 32-bit Intel processor (IA32)
Pentium 4 | 2004 | 2.8-3.8 GHz | First 64-bit Intel processor (x86-64)
Core 2 | 2006 | 1.0-3.5 GHz | First dual-core Intel processor
Core i7 | 2008 | 1.7-3.9 GHz | Support of up to four cores

## Slide 5: Backward Compatibility
Modern x86-64 processors can also run in 32-bit mode.
  There are 32-bit instruction variants.
We can use “gcc” to compile for both 32-bit and 64-bit target machines:
  gcc –m32 myprog.c
  gcc –m64 myprog.c
  By default, 64-bit is assumed.

## Slide 6: Instruction Set Architecture (ISA)
The parts of a processor design that one needs to understand to write assembly language code.
  Data types supported
  Instruction set
  Processor registers
You shall be learning two different ISA’s in this semester:
  x86 in this class (based on CISC)
  MIPS in the COA class (based on RISC)

## Slide 7: Assembly Programmer’s View
CPU
Programmer-Visible State
  PC: Program counter (called Instruction Pointer in x86)
    Called “EIP” (IA32) or “RIP” (x86-64)
  Registers
    Used to temporarily store heavily used data items
  Condition codes
    Store status information about most recent arithmetic operation
    Used for conditional branching
PC
Registers
Memory
Code
Data
Stack
Addresses
Data
Instructions
Condition
Codes

## Slide 8: Turning C Programs into Object Code
text
text
binary
binary
Compiler (gcc -S)
Assembler (gcc or as)
Linker (gcc or ld)
C program (p1.c p2.c)
Asm program (p1.s p2.s)
Object program (p1.o p2.o)
Executable program (p)
Static libraries (.a)
  C code in files p1.c p2.c
  Compile with command: gcc –O1 p1.c p2.c -o p
    Use basic optimizations (-O1)

## Slide 9: Intel 64-bit Registers
GPRs: Sixteen 64-bit integer registers
  rax, rbx, rcx, rdx, rsp, rbp, rsi, rdi, r8, r9, r10, r11, r12, r13, r14, r15
FPRs: Eight 80-bit floating-point registers
  r0, r1, r2, r3, r4, r5, r6, r7
MMXs: Eight 64-bit SIMD registers
  mm0, mm1, mm2, mm3, mm4, mm5, mm6, mm7
XMMs: Sixteen 128-bit SSE registers (Streaming SIMD Extensions)
  xmm0, xmm1, xmm2, xmm3, …, xmm15

## Slide 10: Special Registers
64-bit program counter or instruction pointer (rip)
Segment registers (CS, DS, SS, ES, FS, GS)
64-bit condition flag register (zero, sign, carry, etc.)
Control register, Debug register, etc.

## Slide 11: Main Memory Address
48-bit virtual/logical address – generated by the CPU.
  The width of any x86-64 address register is 64 bits.
  Most significant 17 bits are either all 0’s or all 1’s.
  Thus, logical address size is 64 – 18 = 48 bits.
Depending on the processor, the 48-bit logical address is translated to 36 to 40 bits of physical (main memory) address.

## Slide 12: Register Usage Convention
GPR (64-bit) | Usage Convention
rax | Return value from a function
rbx | Callee saved
rcx | 4th argument to a function
rdx | 3rd argument to a function Return value from a function
rsi | 2nd argument to a function
rdi | 1st argument to a function
rbp | Callee saved
rsp | Hardware stack pointer
GPR (64-bit) | Usage Convention
r8 | 5th argument to a function
r9 | 6th argument to a function
r10 | Callee saved
r11 | Reserved for linker
r12 | Reserved for C
r13 | Callee saved
r14 | Callee saved
r15 | Callee saved
Function return address is at the top of the stack.
For 32-bit, use “eax” instead of “rax”, etc.

## Slide 13: Compiling a C program
Suppose a program is written as two files: main.c and fact.c
  gcc –Wall –S main.c  main.s
  gcc –Wall –c main.c  main.o
  gcc –Wall –S fact.c  fact.s
  gcc –Wall –c fact.c  fact.o
  gcc main.o fact.o  a.out

## Slide 14: Conventions Followed

## Slide 15
According to the convention:
  “ah” or “al” denotes an 8-bit register
  “ax” denotes a 16-bit register
  “eax” denotes a 32-bit register
  “rax” denotes a 64-bit register
Either “e” or “r” type registers will be used in the assembly code depending on whether you are using 32-bit or 64-bit instructions.

## Slide 16: Various Addressing Modes
Mem[x]
56
rbx
Mem[rsp]
Mem[rbp-8]
Mem[rbx-16+rcx*8]

## Slide 17: Mechanism of Function Call and Return

## Slide 18
main()
{
……
x = gcd (a, b);
……
}
int gcd (int x, int y)
{
……
……
return (result);
}
Return Addr
Return Value
Local
Variables
Before call
After call
After return
STACK
Activation record

## Slide 19
main()
{
……
x=ncr(a,b);
……
}
int ncr (int n,int r)
{
return (fact(n)/
fact(r)/fact(n-r));
}
LV1, RV1, RA1
Before call
Call “fact”
“ncr” returns
int fact (int n)
{
………
return(result);
}
3 times
LV1, RV1, RA1
“fact” returns
LV1, RV1, RA1
LV2, RV2, RA2
Call “ncr”
3 times

## Slide 20: Compiling Into Assembly
Generated IA32 Assembly
sum:
pushl %ebp // Save ebp in stack
movl %esp,%ebp // ebp = esp
movl 12(%ebp),%eax // eax = Mem [ebp + 12]
addl 8(%ebp),%eax // eax += Mem[ebp + 8]
popl %ebp // Restore ebp from stack
ret
int sum (int x, int y)
{
int t = x + y;
return t;
}
C Code
x
y
ebp
esp
RA

## Slide 21: “leave” and “enter” Instructions
The “enter” instruction sets up a stack frame by first pushing “rbp” into the stack and then copying “rsp” into “rbp”.
  “gcc” uses the following code segment instead of “enter”:
  pushq %rbp
  movq %rsp, %rbp
  subq $n, %rsp // Allocate space on stack
The “leave” instruction does the opposite: it copies “rbp” to “rsp” and then pops the old “rbp” from the stack.

## Slide 22: Assembler Directives
Words starting with a “.” are assembler directives.
  They do not correspond to machine instructions, but some information that are required by the assembler to generate machine code.
Examples:
  .file, .text, .globl, .type, .string, .section, .size
  .cfi_startproc, .cfi_def_cfa_offset, .cfi_offset, .cfi_endproc, etc.
What are “.cfi” directives?
  Current Frame Index, used for exception handling on some machines.
  To prevent these from appearing in the .s file, use the command:
  gcc –Wall –fno-asynchronous-unwind-tables –S myfile.c

## Slide 23: Some Illustrative Examples

## Slide 24
#include <stdio.h>
int main()
{
int a, b, c;
a = 20; b = 50;
c = a + b;
printf ("\nSum is %d", c);
return 0;
}
main:
pushq %rbp
movq %rsp, %rbp
subq $16, %rsp
movl $20, -12(%rbp)
movl $50, -8(%rbp)
movl -12(%rbp), %edx
movl -8(%rbp), %eax
addl %edx, %eax
movl %eax, -4(%rbp)
movl -4(%rbp), %eax
movl %eax, %esi
movl $.LC0, %edi
movl $0, %eax
call printf
movl $0, %eax
leave
ret
.file "prog1.c"
.text
.section .rodata
.LC0:
.string "\nSum is %d"
.text
.globl main
.type main, @function
Example 1

## Slide 25
int sum (int x, int y)
{
int t = x + y;
return t;
}
_sum:
pushq %rbp
movq %rsp, %rbp
movl %edi, -4(%rbp)
movl %esi, -8(%rbp)
movl -4(%rbp), %esi
addl -8(%rbp), %esi
movl %esi, -12(%rbp)
movl -12(%rbp), %eax
popq %rbp
retq
Example 2
Note:
rdi/edi and rsi/esi contains the 1st and 2nd arguments to a function.
rax/eax will contain the return value from the function.

## Slide 26
#include <stdio.h>
int fact (int);
int main()
{
int n = 7, val;
val = fact(n);
printf ("\nFact (%d) is %d", n, val);
return 0;
}
int fact (int a)
{
int prod, i;
prod = 1;
for (i=1; i<=a; i++)
prod *= i;
return prod;
}
Example 3

## Slide 27
.file "prog2.c"
.text
.section .rodata
.LC0:
.string "\nFact (%d) is %d"
.text
.globl main
.type main, @function
main:
.LFB0:
pushq %rbp
movq %rsp, %rbp
subq $16, %rsp
movl $7, -8(%rbp)
movl -8(%rbp), %eax
movl %eax, %edi
call fact
movl %eax, -4(%rbp)
movl -4(%rbp), %edx
movl -8(%rbp), %eax
movl %eax, %esi
movl $.LC0, %edi
movl $0, %eax
call printf
movl $0, %eax
leave
ret
int main()
{
int n = 7, val;
val = fact(n);
printf ("\nFact (%d) is %d", n, val);
return 0;
}

## Slide 28
.LFE0:
.size main, .-main
.globl fact
.type fact, @function
fact:
.LFB1:
pushq %rbp
movq %rsp, %rbp
movl %edi, -20(%rbp)
movl $1, -8(%rbp)
movl $1, -4(%rbp)
jmp .L4
.L5:
movl -8(%rbp), %eax
imull -4(%rbp), %eax
movl %eax, -8(%rbp)
addl $1, -4(%rbp)
.L4:
movl -4(%rbp), %eax
cmpl -20(%rbp), %eax
jle .L5
movl -8(%rbp), %eax
popq %rbp
ret
int fact (int a)
{
int prod, i;
prod = 1;
for (i=1; i<=a; i++)
prod *= i;
return prod;
}

## Slide 29
#include <stdio.h>
int fact (int);
int ncr (int, int);
int main()
{
int n = 7, r = 3, result;
result = ncr(n,r);
printf ("\nncr(%d,%d) is %d", n, r, result);
return 0;
}
int ncr (int a, int b)
{
return (fact(a) / fact(b) / fact(a-b));
}
int fact (int a)
{
int prod, i;
if (a == 0) return 1;
prod = 1;
for (i=1; i<=a; i++)
prod *= i;
return prod;
}
Example 4

## Slide 30
.file "prog3.c"
.text
.section .rodata
.LC0:
.string "\nncr(%d,%d) is %d"
.text
.globl main
.type main, @function
main:
.LFB0:
pushq %rbp
movq %rsp, %rbp
subq $16, %rsp
movl $7, -12(%rbp)
movl $3, -8(%rbp)
movl -8(%rbp), %edx
movl -12(%rbp), %eax
movl %edx, %esi
movl %eax, %edi
call ncr
movl %eax, -4(%rbp)
movl -4(%rbp), %ecx
movl -8(%rbp), %edx
movl -12(%rbp), %eax
movl %eax, %esi
movl $.LC0, %edi
movl $0, %eax
call printf
movl $0, %eax
leave
ret
int main()
{
int n = 7, r = 3, result;
result = ncr(n,r);
printf ("\nncr(%d,%d) is %d",
n, r, result);
return 0;
}

## Slide 31
ncr:
pushq %rbp
movq %rsp, %rbp
pushq %rbx
subq $24, %rsp
movl %edi, -20(%rbp)
movl %esi, -24(%rbp)
movl -20(%rbp), %eax
movl %eax, %edi
call fact
movl %eax, %ebx
movl -24(%rbp), %eax
movl %eax, %edi
call fact
movl %eax, %ecx
movl %ebx, %eax
cltd
idivl %ecx
movl %eax, %ebx
movl -20(%rbp), %eax
subl -24(%rbp), %eax
movl %eax, %edi
call fact
movl %eax, %esi
movl %ebx, %eax
cltd
idivl %esi
addq $24, %rsp
popq %rbx
popq %rbp
ret
int ncr (int a, int b)
{
return (fact(a) /
fact(b) / fact(a-b));
}

## Slide 32
fact:
pushq %rbp
movq %rsp, %rbp
movl %edi, -20(%rbp)
cmpl $0, -20(%rbp)
jne .L6
movl $1, %eax
jmp .L7
.L6:
movl $1, -8(%rbp)
movl $1, -4(%rbp)
jmp .L8
.L9:
movl -8(%rbp), %eax
imull -4(%rbp), %eax
movl %eax, -8(%rbp)
addl $1, -4(%rbp)
.L8:
movl -4(%rbp), %eax
cmpl -20(%rbp), %eax
jle .L9
movl -8(%rbp), %eax
.L7:
popq %rbp
ret
int fact (int a)
{
int prod, i;
if (a == 0) return 1;
prod = 1;
for (i=1; i<=a; i++)
prod *= i;
return prod;
}

## Slide 33
#include <stdio.h>
void bubble_sort (int[], int);
void swap (int*, int*);
int main()
{
int mydata[] = {20, 12, 40, 10, 70,
30, 50, 80, 5, 25};
bubble_sort (mydata, 10);
printf ("\nSorted list: ");
for (int i=0; i<10; i++)
printf (" %d", mydata[i]);
printf ("\n");
return 0;
}
void bubble_sort (int data[], int n)
{
int i, j;
for (i=0; i<(n-1); i++)
for (j=0; j<(n-i-1); j++)
if (data[j] > data[j+1])
swap (&data[j], &data[j+1]);
}
void swap(int *xp, int *yp)
{
int temp = *xp;
*xp = *yp;
*yp = temp;
}
Example 5

## Slide 34
main:
.LFB0:
pushq %rbp
movq %rsp, %rbp
subq $64, %rsp
movq %fs:40, %rax
movq %rax, -8(%rbp)
xorl %eax, %eax
movl $20, -48(%rbp)
movl $12, -44(%rbp)
movl $40, -40(%rbp)
movl $10, -36(%rbp)
movl $70, -32(%rbp)
movl $30, -28(%rbp)
movl $50, -24(%rbp)
movl $80, -20(%rbp)
movl $5, -16(%rbp)
movl $25, -12(%rbp)
leaq -48(%rbp), %rax
movl $10, %esi
movq %rax, %rdi
call bubble_sort
movl $.LC0, %edi
movl $0, %eax
call printf
movl $0, -52(%rbp)
jmp .L2
.L3:
movl -52(%rbp), %eax
cltq
movl -48(%rbp,%rax,4), %eax
movl %eax, %esi
movl $.LC1, %edi
movl $0, %eax
call printf
addl $1, -52(%rbp)
.L2:
cmpl $9, -52(%rbp)
jle .L3
movl $10, %edi
call putchar
movl $0, %eax
movq -8(%rbp), %rdx
xorq %fs:40, %rdx
je .L5
call __stack_chk_fail
.L5:
leave
ret

## Slide 35
bubble_sort:
.LFB1:
pushq %rbp
movq %rsp, %rbp
subq $32, %rsp
movq %rdi, -24(%rbp)
movl %esi, -28(%rbp)
movl $0, -8(%rbp)
jmp .L7
.L11:
movl $0, -4(%rbp)
jmp .L8
.L10:
movl -4(%rbp), %eax
cltq
leaq 0(,%rax,4), %rdx
movq -24(%rbp), %rax
addq %rdx, %rax
movl (%rax), %edx
movl -4(%rbp), %eax
cltq
addq $1, %rax
leaq 0(,%rax,4), %rcx
movq -24(%rbp), %rax
addq %rcx, %rax
movl (%rax), %eax
.L7:
movl -28(%rbp), %eax
subl $1, %eax
cmpl %eax, -8(%rbp)
jl .L11
nop
leave
ret
cmpl %eax, %edx
jle .L9
movl -4(%rbp), %eax
cltq
addq $1, %rax
leaq 0(,%rax,4), %rdx
movq -24(%rbp), %rax
addq %rax, %rdx
movl -4(%rbp), %eax
cltq
leaq 0(,%rax,4), %rcx
movq -24(%rbp), %rax
addq %rcx, %rax
movq %rdx, %rsi
movq %rax, %rdi
call swap
.L9:
addl $1, -4(%rbp)
.L8:
movl -28(%rbp), %eax
subl -8(%rbp), %eax
subl $1, %eax
cmpl %eax, -4(%rbp)
jl .L10
addl $1, -8(%rbp)

## Slide 36
swap:
pushq %rbp
movq %rsp, %rbp
movq %rdi, -8(%rbp)
movq %rsi, -16(%rbp)
movq -8(%rbp), %rsi
movl (%rsi), %eax
movl %eax, -20(%rbp)
movq -16(%rbp), %rsi
movl (%rsi), %eax
movq -8(%rbp), %rsi
movl %eax, (%rsi)
movl -20(%rbp), %eax
movq -16(%rbp), %rsi
movl %eax, (%rsi)
popq %rbp
ret
void swap(int *xp, int *yp)
{
int temp = *xp;
*xp = *yp;
*yp = temp;
}
*yp
*xp
rbp
-16(%rbp)
-8(%rbp)
0(%rbp)
temp
-20(%rbp)

## Slide 37
int fact (int n)
{
if (n == 0) return 1;
else
return (n * fact(n-1));
}
fact:
.LFB0:
pushq %rbp
movq %rsp, %rbp
subq $16, %rsp
movl %edi, -4(%rbp)
cmpl $0, -4(%rbp)
jne .L2
movl $1, %eax
jmp .L3
.L2:
movl -4(%rbp), %eax
subl $1, %eax
movl %eax, %edi
call fact
imull -4(%rbp), %eax
.L3:
leave
ret
Example 6

## Slide 38: Thank you